Solar Energy – National Geographic

National Geographic, “Solar Energy”, <http://education.nationalgeographic.com/education/encyclopedia/solar-energy/?ar_a=1> accessed April 10, 2015

Solar energy is any type of energy generated by the sun.

Solar energy is created by nuclear fusion that takes place in the sun. Fusion occurs when protons of hydrogen atoms violently collide in the sun’s core and fuse to create a helium atom. 

This process, known as a PP (proton-proton) chain reaction, emits an enormous amount of energy. In its core, the sun fuses about 620 million metric tons of hydrogen every second. The PP chain reaction occurs in other stars that are about the size of our sun, and provides them with continuous energy and heat. The temperature for these stars is around 4 million degrees on the Kelvin scale (about 4 million degrees Celsius, 7 million degrees Fahrenheit).
 
In stars that are about 1.3 times bigger than the sun, the CNO cycle drives the creation of energy. The CNO cycle also converts hydrogen to helium, but relies on carbon, nitrogen, and oxygen (C, N, and O) to do so. Currently, less than 2% of the sun’s energy is created by the CNO cycle. 

Nuclear fusion by the PP chain reaction or CNO cycle releases tremendous amounts of energy in the form of waves and particles. Solar energy is constantly flowing away from the sun and throughout the solar system. Solar energy warms the Earth, causes wind and weather, and sustains plant and animal life.

The energy, heat, and light from the sun flow away in the form of electromagnetic radiation (EMR). 

The electromagnetic spectrum exists as waves of different frequencies and wavelengths. The frequency of a wave represents how many times the wave repeats itself in a certain unit of time. Waves with very short wavelengths repeat themselves several times in a given unit of time, so they are high-frequency. In contrast, low-frequency waves have much longer wavelengths.  

The vast majority of electromagnetic waves are invisible to us. The most high-frequency waves emitted by the sun are gamma rays, X-rays, and ultraviolet radiation (UV rays). The most harmful UV rays are almost completely absorbed by Earth’s atmosphere. Less potent UV rays travel through the atmosphere, and can cause sunburn.

The sun also emits infrared radiation, whose waves are much lower-frequency. Most heat from the sun arrives as infrared energy.

Sandwiched between infrared and UV is the visible spectrum, which contains all the colors we see on Earth. The color red has the longest wavelengths (closest to infrared), and violet (closest to UV) the shortest.

Harnessing Solar Energy

Solar energy is a renewable resource, and many technologies can harvest it directly for use in homes, businesses, schools, and hospitals. Some solar energy technologies include photovoltaic cells and panels, concentrated solar energy, and solar architecture.

There are different ways of capturing solar radiation and converting it into usable energy. The methods use either active solar energy or passive solar energy.

Active solar technologies use electrical or mechanical devices to actively convert solar energy into another form of energy, most often heat or electricity. Passive solar technologies do not use any external devices. Instead, they take advantage of the local climate to heat structures during the winter, and reflect heat during the summer. 

Photovoltaics

Photovoltaics is a form of active solar technology that was discovered in 1839 by 19-year-old French physicist Alexandre-Edmond Becquerel. Becquerel discovered that when he placed silver-chloride in an acidic solution and exposed it to sunlight, the platinum electrodes attached to it generated an electric current. This process of generating electricity directly from solar radiation is called the photovoltaic effect, or photovoltaics.

Today, photovoltaics is probably the most familiar way to harness solar energy. Photovoltaic arrays usually involve solar panels, a collection of dozens or even hundreds of solar cells. 

Each solar cell contains a semiconductor, usually made of silicon. When the semiconductor absorbs sunlight, it knocks electrons loose. An electrical field directs these loose electrons into an electric current, flowing in one direction. Metal contacts at the top and bottom of a solar cell direct that current to an external object. The external object can be as small as a solar-powered calculator or as large as a power station.

Photovoltaics was first widely used on spacecraft. Many satellites, including the International Space Station, feature wide, reflective “wings” of solar panels. The ISS has two solar array wings (SAWs), each using about 33,000 solar cells. These photovoltaic cells supply all electricity to the ISS, allowing astronauts to operate the station, safely live in space for months at a time, and conduct scientific and engineering experiments.

Photovoltaic power stations have been built all over the world. The largest stations are in the United States, India, and China. These power stations emit hundreds of megawatts of electricity, used to supply homes, businesses, schools, and hospitals.

Photovoltaic technology can also be installed on a smaller scale. Solar panels and cells can be fixed to the roofs or exterior walls of buildings, supplying electricity for the structure. They can be placed along roads to light highways. Solar cells are small enough to power even smaller devices, such as calculators, parking meters, trash compactors, and water pumps. 

Concentrated Solar Energy

Another type of active solar technology is concentrated solar energy or concentrated solar power (CSP). CSP technology uses lenses and mirrors to focus (concentrate) sunlight from a large area into a much smaller area. This intense area of radiation heats a fluid, which in turn generates electricity or fuels another process. 

Solar furnaces are an example of concentrated solar power. There are many different types of solar furnaces, including solar power towers, parabolic troughs, and Fresnel reflectors. They use the same general method to capture and convert energy.

Solar power towers use heliostats, flat mirrors that turn to follow the sun’s arc through the sky. The mirrors are arranged around a central “collector tower,” and reflect sunlight into a concentrated ray of light that shines on a focal point on the tower. 

In previous designs of solar power towers, the concentrated sunlight heated a container of water, which produced steam that powered a turbine. More recently, some solar power towers use liquid sodium, which has a higher heat capacity and retains heat for a longer period of time. This means that the fluid not only reaches temperatures of 773 to 1,273 K (500 to 1,000° C or 932 to 1,832° F), but it can continue to boil water and generate power even when the sun is not shining. 

Parabolic troughs and Fresnel reflectors also use CSP, but their mirrors are shaped differently. Parabolic mirrors are curved, with a shape similar to a saddle. Fresnel reflectors use flat, thin strips of mirror to capture sunlight and direct it onto a tube of liquid. Fresnel reflectors have more surface area than parabolic troughs and can concentrate the sun’s energy to about 30 times its normal intensity.

Concentrated solar power plants were first developed in the 1980s. The largest facility in the world is a series of plants in California’s Mojave Desert. This Solar Energy Generating System (SEGS) generates more than 650 gigawatt-hours of electricity every year. Other large and effective plants have been developed in Spain and India.

Concentrated solar power can also be used on a smaller scale. It can generate heat for solar cookers, for instance. People in villages all over the world use solar cookers to boil water for sanitation and to cook food.

Solar cookers provide many advantages over wood-burning stoves: They are not a fire hazard, do not produce smoke, do not require fuel, and reduce habitat loss in forests where trees would be harvested for fuel. Solar cookers also allow villagers to pursue time for education, business, health, or family during time that was previously used for gathering firewood. Solar cookers are used in areas as diverse as Chad, Israel, India, and Peru.

Solar Architecture 

Throughout the course of a day, solar energy is part of the process of thermal convection, or the movement of heat from a warmer space to a cooler one. When the sun rises, it begins to warm objects and material on Earth. Throughout the day, these materials absorb heat from solar radiation. At night, when the sun sets and the atmosphere has cooled, the materials release their heat back into the atmosphere. 

Passive solar energy techniques take advantage of this natural heating and cooling process.

Homes and other buildings use passive solar energy to distribute heat efficiently and inexpensively. Calculating a building’s “thermal mass” is an example of this. A building’s thermal mass is the bulk of material heated throughout the day. Examples of a building’s thermal mass are wood, metal, concrete, clay, stone, or mud. At night, the thermal mass releases its heat back into the room. Effective ventilation systems—hallways, windows, and air ducts—distribute the warmed air and maintain a moderate, consistent indoor temperature. 

Passive solar technology is often involved in the design of a building. For example, in the planning stage of construction, the engineer or architect may align the building with the sun’s daily path to receive desirable amounts of sunlight. This method takes into account the latitude, altitude, and typical cloud cover of a specific area. In addition, buildings can be constructed or retrofitted to have thermal insulation, thermal mass, or extra shading. 

Other examples of passive solar architecture are cool roofs, radiant barriers, and green roofs. Cool roofs are painted white, and reflect the sun’s radiation instead of absorbing it. The white surface reduces the amount of heat that reaches the interior of the building, which in turn reduces the amount of energy that is needed to cool the building.

Radiant barriers work similarly to cool roofs. They provide insulation with highly reflective materials, such as aluminum foil. The foil reflects, instead of absorbs, heat, and can reduce cooling costs up to 10%. In addition to roofs and attics, radiant barriers may also be installed beneath floors.

Solar Energy and People

Since sunlight only shines for about half of the day in most parts of the world, solar energy technologies have to include methods of storing the energy during dark hours. 

Thermal mass systems use paraffin wax or various forms of salt to store the energy in the form of heat. Photovoltaic systems can send excess electricity to the local power grid, or store the energy in rechargeable batteries.

There are many pros and cons to using solar energy. 

Advantages
A major advantage to using solar energy is that it is a renewable resource. We will have a steady, limitless supply of sunlight for another 5 billion years. In one hour, the Earth’s atmosphere receives enough sunlight to power the electricity needs of every human being on Earth for a year. 

Solar energy is clean. After the solar technology equipment is constructed and put in place, solar energy does not need fuel to work. It also does not emit greenhouse gases or toxic materials. Using solar energy can drastically reduce the impact we have on the environment.

There are locations where solar energy is practical. Homes and buildings in areas with high amounts of sunlight and low cloud cover have the opportunity to harness the sun’s abundant energy. 

Solar cookers provide an excellent alternative to cooking with wood-fired stoves—on which 2 billion people still rely. Solar cookers provide a cleaner and safer way to sanitize water and cook food.

Solar energy complements other renewable sources of energy, such as wind or hydroelectric energy.

Homes or businesses that install successful solar panels can actually produce excess electricity. These homeowners or businessowners can sell energy back to the electric provider, reducing or even eliminating power bills.

Disadvantages
The main deterrent to using solar energy is the required equipment. Solar technology equipment is expensive. Purchasing and installing the equipment can cost tens of thousands of dollars for individual homes. Although the government often offers reduced taxes to people and businesses using solar energy, and the technology can eliminate electricity bills, the initial cost is too steep for many to consider.

Solar energy equipment is also heavy. In order to retrofit or install solar panels on the roof of a building, the roof must be strong, large, and oriented toward the sun’s path.

Both active and passive solar technology depend on factors that are out of our control, such as climate and cloud cover. Local areas must be studied to determine whether or not solar power would be effective in that area. 

Sunlight must be abundant and consistent for solar energy to be an efficient choice. In most places on Earth, sunlight’s variability makes it difficult to implement as the only source of energy.

Wind Energy

National Geographic, “Wind Energy” <http://education.nationalgeographic.com/education/encyclopedia/wind-energy/?ar_a=1> accessed April 10, 2015.

Wind energy is produced by the movement of air (wind) and converted into power for human use. Wind has been used as a source of energy for more than a thousand years, but was replaced by fossil fuels for much of the 20th century. Today, wind is making a comeback as a source of electricity and power. 

Wind energy is produced with wind turbines—tall, tubular towers with blades rotating at the top. When the wind turns the blades, the blades turn a generator and create electricity. Wind turbines can have a horizontal or vertical axis. The turbines do not actually produce wind energy. The blades turn, convert the energy of wind into rotational energy, a form of mechanical energy, and this energy is in turn converted into electrical energy.

Horizontal-axis wind turbines (HAWTs) are the most familiar type of electricity-producing windmill. Most have three large blades that spin parallel to their towers, where the main rotor and generator are located.

Most HAWT arrays are painted white, to promote visibility to low-flying aircraft. They stand about 60 to 90 meters (200 to 300 feet) tall, and the blades rotate at 10 to 20 rotations a minute.

The enormous, stiff blades on a horizontal-axis wind turbine usually face the wind (upwind). A wind vane or wind sensor determines which way the wind is blowing, and turns the turbine to face the oncoming wind.

Vertical-axis wind turbines (VAWTs) have varied, unusually shaped blades that rotate in complete circles around their tower. The main rotor and generator are located near the ground, making maintenance easier and less expensive. VAWTs do not have to be upwind to generate electricity.

Vertical-axis wind turbines can be much smaller than their horizontal counterparts. Standing only 5 meters (15 feet) tall, these VAWTs can be installed on the roofs of buildings.

Turbines cannot operate at every wind speed. If winds are too strong, they can be damaged. Therefore, the turbine has an automatic controller that turns on when winds are blowing at prime speed for generating electricity. This speed is usually 13 to 90 kilometers per hour (8 to 55 miles per hour). If the winds become stronger than that, the controller turns the turbine off.

Wind Farms

In order to generate a large amount of electricity, wind turbines are often constructed in large groups called wind farms. Wind farms are made up of hundreds of turbines, spaced out over hundreds of acres.
One of the largest wind farms in the world is Jaisalmer Wind Park, a series of connected facilities in the state of Rajasthan, India. In April 2012, Jaisalmer produced 1,064 megawatts of electricity, more than any other onshore wind farm in the world.

Wind farms are often located in agricultural areas, where the land between the turbines can still be used for farming. Grazing animals are unaffected by the large, slow-moving turbines.

In the U.S., the “Corn Belt” overlaps with the “Wind Belt,” an area across the Midwest that is ideal for harvesting crops and wind. Wind turbines tower over acres of corn, soy, and alfalfa in the states of Iowa, Nebraska, and Kansas. Some scientists suggest wind turbines may even improve the flow of carbon dioxide to surrounding crops.

Wind farms can also be located offshore. These turbines use the stronger, more predictable, and more frequent winds that develop as cool ocean breezes meet warmer continental winds.

The world’s most powerful offshore wind farms harvest the harsh winds off the coasts of Northern Europe. Walney Wind Farm, for example, is a farm of 102 turbines in the Irish Sea off the coast of Cumbria, England. Walney is the largest offshore wind farm in the world, generating 367 megawatts of power.

Technology is also being developed to create wind farms at extremely high altitudes. Jet streams are fast-moving winds that blow through the stratosphere at elevations of 9,754 meters (32,000 feet). Scientists and engineers are developing a wind turbine that would be tethered to the ground like a kite, but float thousands of meters in the air to capture jet streams’ energy for electricity.

Single wind turbines can be purchased by individuals to generate electricity for their home or business. Progressive Field, home of the Cleveland Indians baseball team in Cleveland, Ohio, has an enormous vertical-axis wind turbine. The corkscrew-shaped turbine is expected to generate about 40,000 kilowatt-hours per year, roughly the amount of energy needed to power four homes.

Wind turbines depend on wind, which is inconsistent and can be difficult to predict. Although wind is a renewable resource, its speed and direction change frequently, depending on other conditions of the atmosphere, such as temperature, humidity, and season.

Today, this unpredictability makes it a poor substitute for fossil fuels or more powerful renewable energy sources, such as solar energy. Developing nations such as Brazil and India are industrializing at a quick pace. The industrialized Western world relies on electricity for mass communication as well as commerce. Due to these increasing demands on the power grid, wind can be an excellent supplement to traditional power, but not the dominant component in most regions. 

Advantages
There are many advantages to using the wind’s energy to create electricity.

- Wind cannot be used up—it occurs naturally, whether we harness it for electricity or not.

- Wind is a clean source of fuel. Turbines have no emissions and do not pollute the air. This is globally important as more countries industrialize and increase their demand for electricity for homes, businesses, hospitals, and schools. Many schools in the U.S. state of Iowa, for example, have installed wind turbines. Initial investments in the machinery and equipment have been offset by savings of more than $100,000 a year. The schools also emit millions fewer kilograms of carbon dioxide.

- Wind energy is cheap! It is one of the lowest-priced renewable energy sources. In the U.S., it costs between 4 and 6 cents per kilowatt-hour. That is cheaper than natural gas, although still more expensive than nuclear energy or coal.

- Wind is generated all over the planet, and wind turbines can be installed economically almost everywhere. This makes it a key resource in developing economies. Nuclear energy, for instance, demands a workforce with substantial educational and engineering backgrounds, as well as an initial investment for nuclear power plants. Development of fossil fuel power plants relies on even more factors: the presence of coal, oil, or gas; the equipment and technology to refine it; and the finances to import or export the raw or refined goods. Nepal, for example, is a developing country with no fossil fuel resources, but it is rich in windy Himalayan mountain passes. Nepalese leaders are developing a policy to invest in wind farm projects using local materials. This would expand the nation’s power grid and allow for greater industrial development.

Challenges
There are also many challenges of using wind energy:

- Even though wind energy is cheap, the initial cost to build the wind farm or install a turbine still costs more than fossil-fuel generators. It may take years to offset the start-up cost.

- Onshore wind farms require acres of land, and must compete with other uses. In the U.S. and Australia, land between turbines is often used for agricultural purposes, and the farmer or rancher who owns the land is paid for renting out sections of his fields. When planning a wind farm in a hilly area, where winds are steady and strong, trees may need to be cut. This destroys habitats of dozens of species and may even impact the larger food web of an area. In Northern Europe, wind farms are often developed in bogs, which are reservoirs of the fossil fuel peat. Developing bogs for the installation of wind turbines may release many kilograms of carbon dioxide and other greenhouse gases.

- Wind turbines can kill bats and birds. Bats’ echolocation does not account for giant spinning blades, and they can be hit. The blades also hit birds, and can scare certain species of birds away from their habitats. Potential solutions may not require sophisticated technology. A study that tracked bat deaths around turbines in Somerset County, Pennsylvania, found that fatalities fell by more than half when turbines simply stopped operating during periods of very low wind activity. Other solutions include using ultraviolet radiation (UV light) to improve the way bats perceive the moving blades, and designing a device that would imitate sounds that bats would avoid.

- Offshore wind farms may impact the marine ecosystem. The seafloor must be disturbed and drilled to establish a wind turbine. Although wind farms are carefully planned to avoid shipping routes and busy harbors, they may still pose a risk for vessels during violent storms.

- Some residents who live near wind farms complain about the noise or appearance of the machinery.

- Locations that produce great amounts of wind are often in remote areas, far away from the cities and people who could use it. Transmission lines have to be built to transfer the electricity to cities.

Geothermal

National Geographic, “Geothermal,” <http://education.nationalgeographic.com/education/encyclopedia/geothermal-energy/?ar_a=1> accessed April 10, 2015.

Geothermal energy is heat that is generated within the Earth. (Geo means “earth,” and thermal means “heat” in Greek.) It is a renewable resource that can be harvested for human use.

About 2,900 kilometers (1,800 miles) below the Earth’s crust, or surface, is the hottest part of our planet: the core. A small portion of the core’s heat comes from the friction and gravitational pull formed when Earth was created more than 4 billion years ago. However, the vast majority of Earth’s heat is constantly generated by the decay of radioactive isotopes, such as potassium-40 and thorium-232. 
 
Isotopes are forms of an element that have a different number of neutrons than regular versions of the element’s atom. Potassium, for instance, has 20 neutrons in its nucleus. Potassium-40, however, has 21 neutrons. As potassium-40 decays, its nucleus changes, emitting enormous amounts of energy (radiation). Potassium-40 most often decays to isotopes of calcium (calcium-40) and argon (argon-40). 

Radioactive decay is a continual process in the core. Temperatures there rise to more than 5,000° Celsius (about 9,000° Fahrenheit). Heat from the core is constantly radiating outward and warming rocks, water, gas, and other geological material. 

Earth’s temperature rises with depth from the surface to the core. This gradual change in temperature is known as the geothermal gradient. In most parts of the world, the geothermal gradient is about 25° C per 1 kilometer of depth (1° F per 77 feet of depth). 

If underground rock formations are heated to about 700-1,300° C (1,300-2,400° F), they can become magma. Magma is molten (partly melted) rock permeated by gas and gas bubbles. Magma exists in the mantle and lower crust, and sometimes bubbles to the surface as lava. 

Magma heats nearby rocks and underground aquifers. Hot water can be released through geysers, hot springs, steam vents, underwater hydrothermal vents, and mud pots. 

These are all sources of geothermal energy. Their heat can be captured and used directly for heat, or their steam can be used to generate electricity. Geothermal energy can be used to heat structures such as buildings, parking lots, and sidewalks. 

Most of the Earth’s geothermal energy does not bubble out as magma, water, or steam. It remains in the mantle, emanating outward at a slow pace and collecting as pockets of high heat. This dry geothermal heat can be accessed by drilling, and enhanced with injected water to create steam. 

Many countries have developed methods of tapping into geothermal energy. Different types of geothermal energy are available in different parts of the world. In Iceland, abundant sources of hot, easily accessible underground water make it possible for most people to rely on geothermal sources as a safe, dependable, and inexpensive source of energy. Other countries, such as the U.S., must drill for geothermal energy at greater cost.

Harvesting Geothermal Energy: Heating and Cooling

Low-Temperature Geothermal Energy
Almost anywhere in the world, geothermal heat can be accessed and used immediately as a source of heat. This heat energy is called low-temperature geothermal energy. Low-temperature geothermal energy is obtained from pockets of heat about 150° C (302° F). Most pockets of low-temperature geothermal energy are found just a few meters below ground.

Low-temperature geothermal energy can be used for heating greenhouses, homes, fisheries, and industrial processes. Low-temperature energy is most efficient when used for heating, although it can sometimes be used to generate electricity.

People have long used this type of geothermal energy for engineering, comfort, healing, and cooking. Archaeological evidence shows that 10,000 years ago, groups of Native Americans gathered around naturally occurring hot springs to recuperate or take refuge from conflict. In the third century BCE, scholars and leaders warmed themselves in a hot spring fed by a stone pool near Lishan, a mountain in central China. One of the most famous hot spring spas is in the appropriately named town of Bath, England. Starting construction in about 60 CE, Roman conquerors built an elaborate system of steam rooms and pools using heat from the region’s shallow pockets of low-temperature geothermal energy.

- The hot springs of Chaudes Aigues, France, have provided a source of income and energy for the town since the 1300s. Tourists flock to the town for its elite spas. The low-temperature geothermal energy also supplies heat to homes and businesses. 

The United States opened its first geothermal district heating system in 1892 in Boise, Idaho. This system still provides heat to about 450 homes.

Co-Produced Geothermal Energy
Co-produced geothermal energy technology relies on other energy sources. This form of geothermal energy uses water that has been heated as a byproduct in oil and gas wells. 

In the United States, about 25 billion barrels of hot water are produced every year as a byproduct. In the past, this hot water was simply discarded. Recently, it has been recognized as a potential source of even more energy: Its steam can be used to generate electricity to be used immediately or sold to the grid. 

One of the first co-produced geothermal energy projects was initiated at the Rocky Mountain Oilfield Testing Center in the U.S. state of Wyoming. The facility continues to produce about 200 kilowatts of power using fluids discarded from nearby petroleum and natural gas wells. 
Newer technology has allowed co-produced geothermal energy facilities to be portable. Although still in experimental stages, mobile power plants hold tremendous potential for isolated or impoverished communities.

Geothermal Heat Pumps
Geothermal heat pumps (GHPs) take advantage of the Earth’s heat, and can be used almost anywhere in the world. GHPs are drilled about 3 to 90 meters (10 to 300 feet) deep, much shallower than most oil and natural gas wells. GHPs do not require fracturing bedrock to reach their energy source.

A pipe connected to a GHP is arranged in a continuous loop—called a "slinky loop"—that circles underground and above ground, usually throughout a building. The loop can also be contained entirely underground, to heat a parking lot or landscaped area.

In this system, water or other liquids (such as glycerol, similar to a car’s antifreeze) move through the pipe. During the cold season, the liquid absorbs underground geothermal heat. It carries the heat upward through the building and gives off warmth through a duct system. These heated pipes can also run through hot water tanks and offset water-heating costs. 

During the summer, the GHP system works the opposite way: The liquid in the pipes is warmed from the heat in the building or parking lot, and carries the heat to be cooled underground.

The U.S. Environmental Protection Agency has called geothermal heating the most energy-efficient and environmentally safe heating and cooling system. The largest GHP system was completed in 2012 at Ball State University in Indiana. The system replaced a coal-fired boiler system, and experts estimate the university will save about $2 million a year in heating costs.

Harvesting Geothermal Energy: Electricity

In order to obtain enough energy to generate electricity, geothermal power plants rely on heat that exists a few kilometers below the surface of the Earth. In some areas, the heat can naturally exist underground as pockets steam or hot water. However, most areas need to be “enhanced” with injected water to create steam.

Dry-Steam Power Plants
Dry-steam power plants take advantage of natural underground sources of steam. The steam is piped directly to a power plant, where it is used to fuel turbines and generate electricity. 

Dry steam is the oldest type of power plant to generate electricity using geothermal energy. The first dry-steam power plant was constructed in Larderello, Italy, in 1911. Today, the dry-steam power plants at Larderello continue to supply electricity to more than a million residents of the area. 

There are only two known sources of underground steam in the United States: Yellowstone National Park in Wyoming and The Geysers in California. Since Yellowstone is a protected area, The Geysers is the only place where a dry-steam power plant is in use. It is one of the largest geothermal energy complexes in the world, and provides about a fifth of all renewable energy in California.

Flash-Steam Power Plant
Flash-steam power plants use naturally occurring sources of underground hot water and steam. Water that is hotter than 182° C (360° F) is pumped into a low-pressure area. Some of the water “flashes,” or evaporates rapidly into steam, and is funneled out to power a turbine and generate electricity. Any remaining water can be flashed in a separate tank to extract more energy. 

Flash-steam power plants are the most common type of geothermal power plants. The volcanically active island nation of Iceland supplies nearly all its electrical needs through a series of flash-steam geothermal power plants. The steam and excess warm water produced by the flash-steam process heat icy sidewalks and parking lots in the frigid Arctic winter.

The islands of the Philippines also sit over a tectonically active area, the "Ring of Fire" that rims the Pacific Ocean. Government and industry in the Philippines have invested in flash-steam power plants, and today the nation is second only to the United States in its use of geothermal energy. In fact, the largest single geothermal power plant is a flash-steam facility in Malitbog, Philippines. 

Binary Cycle Power Plants
Binary cycle power plants use a unique process to conserve water and generate heat. Water is heated underground to about 107°-182° C (225°-360° F). The hot water is contained in a pipe, which cycles above ground. The hot water heats a liquid organic compound that has a lower boiling point than water. The organic liquid creates steam, which flows through a turbine and powers a generator to create electricity. The only emission in this process is steam. The water in the pipe is recycled back to the ground, to be re-heated by the Earth and provide heat for the organic compound again.

The Beowawe Geothermal Facility in the U.S. state of Nevada uses the binary cycle to generate electricity. The organic compound used at the facility is an industrial refrigerant (tetrafluoroethane, a greenhouse gas). This refrigerant has a much lower boiling point than water, meaning it is converted into gas at low temperatures. The gas fuels the turbines, which are connected to electrical generators. 

Enhanced Geothermal Systems
The Earth has virtually endless amounts of energy and heat beneath its surface. However, it is not possible to use it as energy unless the underground areas are "hydrothermal." This means the underground areas are not only hot, but also contain liquid and are permeable. Many areas do not have all three of these components. An enhanced geothermal system (EGS) uses drilling, fracturing, and injection to provide fluid and permeability in areas that have hot—but dry—underground rock. 

To develop an EGS, an “injection well” is drilled vertically into the ground. Depending on the type of rock, this can be as shallow as 1 kilometer (0.6 mile) to as deep as 4.5 kilometers (2.8 miles). High-pressure cold water is injected into the drilled space, which forces the rock to create new fractures, expand existing fractures, or dissolve. This creates a reservoir of underground fluid. 

Water is pumped through the injection well and absorbs the rocks’ heat as it flows through the reservoir. This hot water, called brine, is then piped back up to Earth’s surface through a “production well.” The heated brine is contained in a pipe. It warms a secondary fluid that has a low boiling point, which evaporates to steam and powers a turbine. The brine cools off, and cycles back down through the injection well to absorb underground heat again. There are no gaseous emissions besides the water vapor from the evaporated liquid. 

Pumping water into the ground for EGSs can cause seismic activity, or small earthquakes. In Basel, Switzerland, the injection process caused hundreds of tiny earthquakes that grew to more significant seismic activity even after the water injection was halted. This led to the geothermal project being canceled in 2009.

Geothermal Energy and the Environment

Geothermal energy is a renewable resource. The Earth has been emitting heat for about 4.5 billion years, and will continue to emit heat for billions of years into the future because of the ongoing radioactive decay in the Earth’s core. 

However, most wells that extract the heat will eventually cool, especially if heat is extracted more quickly than it is given time to replenish. Larderello, Italy, site of the world’s first electrical plant supplied by geothermal energy, has seen its steam pressure fall by more than 25% since the 1950s. 

Re-injecting water can sometimes help a cooling geothermal site last longer. However, this process can cause “micro-earthquakes.” Although most of these are too small to be felt by people or register on a scale of magnitude, sometimes the ground can quake at more threatening levels and cause the geothermal project to shut down, as it did in Basel, Switzerland.

- Geothermal systems do not require enormous amounts of freshwater. In binary systems, water is only used as a heating agent, and is not exposed or evaporated. It can be recycled, used for other purposes, or released into the atmosphere as non-toxic steam. However, if the geothermal fluid is not contained and recycled in a pipe, it can absorb harmful substances such as arsenic, boron, and fluoride. These toxic substances can be carried to the surface and released when the water evaporates. In addition, if the fluid leaks to other underground water systems, it can contaminate clean sources of drinking water and aquatic habitats.

Advantages
There are many advantages to using geothermal energy either directly or indirectly:
•    Geothermal energy is renewable; it is not a fossil fuel that will be eventually used up. The Earth is continuously radiating heat out from its core, and will continue to do so for billions of years. 
•    Some form of geothermal energy can be accessed and harvested anywhere in the world.
•    Using geothermal energy is relatively clean. Most systems only emit water vapor, although some emit very small amounts of sulfur dioxide, nitrous oxides, and particulates.
•    Geothermal power plants can last for decades and possibly centuries. If a reservoir is managed properly, the amount of extracted energy can be balanced with the rock’s rate of renewing its heat. 
•    Unlike other renewable energy sources, geothermal systems are “baseload.” This means they can work in the summer or winter, and are not dependent on changing factors such as the presence of wind or sun. Geothermal power plants produce electricity or heat 24 hours a day, 7 days a week.
•    The space it takes to build a geothermal facility is much more compact than other power plants. To produce a GWh (a gigawatt hour, or one million kilowatts of energy for one hour, an enormous amount of energy), a geothermal plant uses the equivalent of about 1,046 square kilometers (404 square miles) of land. To produce the same GWh, wind energy requires 3,458 square kilometers (1,335 square miles), a solar photovoltaic center requires 8,384 square kilometers (3,237 square miles), and coal plants use about 9,433 square kilometers (3,642 square miles). 
•    Geothermal energy systems are adaptable to many different conditions. They can be used to heat, cool, or power individual homes, whole districts, or industrial processes.

Disadvantages
Harvesting geothermal energy still poses many challenges:
•    The process of injecting high-pressure streams of water into the Earth can result in minor seismic activity, or small earthquakes.
•    Geothermal plants have been linked to subsidence, or the slow sinking of land. This happens as the underground fractures collapse upon themselves. In some areas of New Zealand, the ground under a geothermal power plant subsides at a rate of almost a half a meter (1.6 feet) every year. This can lead to damaged pipelines, roadways, buildings, and natural drainage systems. 
•    Geothermal plants can release small amounts of greenhouse gases such as hydrogen sulfide and carbon dioxide. 
•    Water that flows through underground reservoirs can pick up trace amounts of toxic elements such as arsenic, mercury, and selenium. These harmful substances can be leaked to water sources if the geothermal system is not properly insulated. 
•    Although the process requires almost no fuel to run, the initial cost of installing geothermal technology is expensive. Developing countries may not have the sophisticated infrastructure or start-up costs to invest in a geothermal power plant. Several facilities in the Philippines, for example, were made possible by investments from American industry and government agencies. Today, the plants are Philippine-owned and operated.

Hydroelectric Energy

National Geographic, “Hydroelectric Energy,” <http://education.nationalgeographic.com/education/encyclopedia/hydroelectric-energy/?ar_a=1> accessed April 11, 2015.

Hydroelectric energy is made by moving water. Hydro comes from the Greek word for water. 

Hydroelectric energy has been in use for thousands of years. Ancient Romans built turbines, which are wheels turned by flowing water. Roman turbines were not used for electricity, but for grinding grains to make flour and breads. 

Water mills provide another source of hydroelectric energy. Water mills, which were common until the Industrial Revolution, are large wheels usually located on the banks of moderately flowing rivers. Water mills generate energy that powers such diverse activities as grinding grain, cutting lumber, or creating hot fires to create steel. 

The first U.S. hydroelectric power plant was built on the Fox River in 1882 in Appleton, Wisconsin. This plant powered two paper mills and one home.

Harnessing Hydroelectricity

To harness energy from flowing water, the water must be controlled. A large reservoir is created, usually by damming a river to create an artificial lake, or reservoir. Water is channeled through tunnels in the dam. 

The energy of water flowing through the dam's tunnels causes turbines to turn. The turbines make generators move. Generators are machines that produce electricity. 

Engineers control the amount of water let through the dam. The process used to control this flow of water is called the intake system. When a lot of energy is needed, most of the tunnels to the turbines are open, and millions of gallons of water flow through them. When less energy is needed, engineers slow down the intake system by closing some of the tunnels. 

During floods, the intake system is helped by a spillway. A spillway is a structure that allows water to flow directly into the river or other body of water below the dam, bypassing all tunnels, turbines, and generators. Spillways prevent the dam and the community from being damaged. Spillways, which look like long ramps, are empty and dry most of the time.

From Water Currents to Electrical Currents

Large, fast-flowing rivers produce the most hydroelectricity. The Columbia River, which forms part of the border between the U.S. states of Washington and Oregon, is a big river that produces massive amounts of hydroelectric energy. 

The Bonneville Dam, one of many dams on the Columbia River, has 20 turbines and generates more than a million watts of power every year. Thats enough energy to power hundreds of thousands of homes and businesses.

Hydroelectric power plants near waterfalls can create huge amounts of energy, too. Water crashing over the fall line is full of energy. A famous example of this is the hydroelectric plant at Niagara Falls, which spans the border between the United States and Canada. 

Hydroelectric energy generated by Niagara Falls is split between the U.S. state of New York and the Canadian province of Ontario. Engineers at Niagara Falls cannot turn the falls off, but they can severely limit the intake and control the amount of water rushing over the waterfall.

The largest hydroelectric power plant in the world is the enormous Three Gorges Dam, which spans the Yangtze River in China. It is 185 meters (607 feet) tall and 115 meters (377 feet) thick at its base. It has 26 turbines and will be able to generate more than a billion watts of power. The Three Gorges Dam is operating, but engineers are still working on the system. They are adding even more turbines and generators to the project.

Hydroelectric Energy and the Environment

Hydroelectricity relies on water, which is a clean, renewable energy source. A renewable source of energy is one that will not run out. Renewable energy comes from natural sources, like wind, sunlight, rain, tides, and geothermal energy (the heat produced inside the Earth). Non-renewable energy sources include coal, oil, and natural gas. 

Water is renewable because the water cycle is continually recycling itself. Water evaporates, forms clouds, and then rains down on the Earth, starting the cycle again.

Reservoirs created by dams can provide large, safe recreational space for a community. Boaters and water skiers can enjoy the lake. Many reservoirs are also stocked with fish. The area around a reservoir is often a protected natural space, allowing campers and hikers to enjoy the natural environment.

Using water as a source of energy is generally a safe environmental choice. Its not perfect, though. Hydroelectric power plants require a dam and a reservoir. These man-made structures may be obstacles for fish trying to swim upstream. Some dams, including the Bonneville Dam, have installed fish ladders to help fish migrate. Fish ladders are a series of wide steps built on the side of the river and dam. The ladder allows fish to slowly swim upstream instead of being totally blocked by the dam. 

Dams flood river banks, destroying wetland habitat for thousands of organisms. Aquatic birds such as cranes and ducks are often at risk, as well as plants that depend on the marshy habitat of a river bank. Operating the power plant may also raise the temperature of the water in the reservoir. Plants and animals near the dam have to adjust to this change or migrate elsewhere. 

The OShaughnessy Dam on the Tuolumne River in the U.S. state of California was one of the first hydroelectric energy projects to draw widespread criticism for its impact on the environment. The dam, constructed in 1913, flooded a region called Hetch Hetchy Valley, part of Yosemite National Park. (The lake created by the OShaughnessy Dam is called the Hetch Hetchy Reservoir.) Environmental coalitions opposed the dam, citing the destruction of the environment and the habitats it provided. However, the power plant provided affordable hydroelectric energy to the booming urban area around San Francisco. 

The Hetch Hetchy Reservoir is still a controversial project. Many people believe the OShaughnessy Dam should be destroyed and the valley returned to its native habitat. Others contend that destroying a source of energy for such a major urban area would reduce the quality of life for residents of the Bay Area. 

There are limits to the amount of hydroelectric energy a dam can provide. The most limiting factor is silt that builds up on the reservoirs bed. This silt is carried by the flowing river, but prevented from reaching its normal destination in a delta or river mouth by the dam. Hundreds of meters of silt build up on the bottom of the reservoir, reducing the amount of water in the facility. Less water means less powerful energy to flow through the systems turbines. Most dams must spend a considerable amount of money to avoid silt build-up, a process called siltation. Some power plants can only provide electricity for 20 or 30 years because of siltation.

Fossil Fuels

National Geographic, “Non-renewable Energy,” <http://education.nationalgeographic.com/education/encyclopedia/non-renewable-energy/?ar_a=1> Accessed April 11, 2015.

Non-renewable energy comes from sources that will run out or will not be replenished in our lifetimes—or even in many, many lifetimes.

Most non-renewable energy sources are fossil fuels: coal, petroleum, and natural gas. Carbon is the main element in fossil fuels. For this reason, the time period that fossil fuels formed (about 360-300 million years ago) is called the Carboniferous Period.

All fossil fuels formed in a similar way. Hundreds of millions of years ago, even before the dinosaurs, Earth had a different landscape. It was covered with wide, shallow seas and swampy forests.

Plants, algae, and plankton grew in these ancient wetlands. They absorbed sunlight and created energy through photosynthesis. When they died, the organisms drifted to the bottom of the sea or lake. There was energy stored in the plants and animals when they died.

Over time, the dead plants were crushed under the seabed. Rocks and other sediment piled on top of them, creating high heat and pressure underground. In this environment, the plant and animal remains eventually turned into fossil fuels (coal, natural gas, and petroleum). Today, there are huge underground pockets (called reservoirs) of these non-renewable sources of energy all over the world.

Advantages and Disadvantages

Fossil fuels are a valuable source of energy. They are relatively inexpensive to extract. They can also be stored, piped, or shipped anywhere in the world.

However, burning fossil fuels is harmful for the environment. When coal and oil are burned, they release particles that can pollute the air, water, and land. Some of these particles are caught and set aside, but many of them are released into the air.

Burning fossil fuels also upsets Earth’s “carbon budget,” which balances the carbon in the ocean, earth, and air. When fossil fuels are combusted (heated), they release carbon dioxide into the atmosphere. Carbon dioxide is a gas that keeps heat in Earth’s atmosphere, a process called the “greenhouse effect.” The greenhouse effect is necessary to life on Earth, but relies on a balanced carbon budget.

The carbon in fossil fuels has been sequestered, or stored, underground for millions of years. By removing this sequestered carbon from the earth and releasing it into the atmosphere, Earth’s carbon budget is out of balance. This contributes to temperatures rising faster than organisms can adapt.

Coal

Coal is a black or brownish rock. We burn coal to create energy. Coal is ranked depending on how much “carbonization” it has gone through. Carbonization is the process that ancient organisms undergo to become coal. About 3 meters (10 feet) of solid vegetation crushed together into .3 meter (1 foot) of coal!

Peat is the lowest rank of coal. It has gone through the least amount of carbonization. It is an important fuel in areas of the world including Scotland, Ireland, and Finland.

Anthracite is the highest rank of coal. Anthracite forms in regions of the world where there have been giant movements of the earth, such as the formation of mountain ranges. The Appalachian Mountains, in the eastern part of the United States, are rich in anthracite.

We mine coal out of the ground so we can burn it for energy. There are two ways that we can mine coal: underground mining and surface mining.

Underground mining is used when the coal is located below the surface of the Earth, sometimes 300 meters (1,000 feet) deep—that’s deeper than most of the Great Lakes! Miners take an elevator down a mineshaft. They operate heavy machinery that cuts the coal out of the Earth and brings it above ground. This can be dangerous work because cutting coal can release dangerous gases. The gases can cause explosions or make it hard for miners to breathe.

Surface mining is used when the coal is located very near the surface of the earth. To get to the coal, companies must first clear the area. They take away the trees and soil. The coal can then be cut out of the ground more easily. Entire habitats are destroyed during this process.

About half the electricity in the United States comes from coal. It gives power to our lights, refrigerators, dishwashers, and most other things we plug in. When coal is burned, it leaves “byproducts” that are also valuable. We use the byproducts to make cement, plastics, roads, and many other things.

Advantages and Disadvantages

Coal is a reliable source of energy. We can rely on it day and night, summer and winter, sunshine or rain, to provide fuel and electricity.

Using coal is also harmful. Mining is one of the most dangerous jobs in the world. Coal miners are exposed to toxic dust and face the dangers of cave-ins and explosions at work.

When coal is burned, it releases many toxic gases and pollutants into the atmosphere. Mining for coal can also cause the ground to cave in and create underground fires that burn for decades at a time.

Natural Gas

Natural gas is another fossil fuel that is trapped underground in reservoirs. It is mostly made up of methane. You may have smelled methane before. The decomposing material in landfills also release methane, which smells like rotten eggs.

There is so much natural gas underground that it is measured in million, billion, or trillion cubic meters.

Natural gas is found in deposits a few hundred meters underground. In order to get natural gas out of the ground, companies drill straight down. However, natural gas does not form in big open pockets. Natural gas is trapped in rock formations that can stretch for kilometers.

To reach natural gas, some companies use a process called “hydraulic fracturing,” or fracking. Hydraulic means they use water, and fracturing means to “split apart.” The process uses high-pressure water to split apart the rocks underground. This releases the natural gas that is trapped in rock formations. If the rock is too hard, they can send acid down the well to dissolve the rock. They can also use tiny grains of glass or sand to prop open the rock and let the gas escape.

We use natural gas for heating and cooking. Natural gas can also be burned to generate electricity. We rely on natural gas to give power to lights, televisions, air conditioners, and kitchen appliances in our homes.

Natural gas can also be turned into a liquid form, called liquid natural gas (LNG). LNG is much cleaner than any other fossil fuels.

Liquid natural gas takes up much less space than the gaseous form. The amount of natural gas that would fit into a big beach ball would fit into a ping-pong ball as a liquid! LNG can be easily stored and used for different purposes. LNG can even be a replacement for gasoline.

Advantages and Disadvantages

Natural gas is relatively inexpensive to extract, and is a “cleaner” fossil fuel than oil or coal. When natural gas is burned, it only releases carbon dioxide and water vapor (which are the exact same gases that we breathe out when we exhale!) This is healthier than burning coal.

However, extracting natural gas can cause environmental problems. Fracturing rocks can cause mini-earthquakes. The high-pressure water and chemicals that are forced underground can also leak to other sources of water. The water sources, used for drinking or bathing, can become contaminated and unsafe.

Nuclear Power

National Geographic, “Nuclear Power,” <http://education.nationalgeographic.com/education/encyclopedia/nuclear-energy/?ar_a=1> accessed April 11, 2015.

Nuclear energy is the energy in the nucleus, or core, of an atom. Atoms are tiny units that make up all matter in the universe. Energy is what holds the nucleus together. There is a huge amount of power in an atoms dense nucleus. In fact, the power that holds the nucleus together is officially called the "strong force.”

Nuclear energy can be used to create electricity, but it must first be released from the atom. In nuclear fission, atoms are split to release the energy. 

A nuclear reactor, or power plant, is a series of machines that can control nuclear fission to produce electricity. The fuel that nuclear reactors use to produce nuclear fission is pellets of the element uranium. In a nuclear reactor, atoms of uranium are forced to break apart. As they split, the atoms release tiny particles called fission products. Fission products cause other uranium atoms to split, starting a chain reaction. The energy released from this chain reaction creates heat.

The heat created by nuclear fission warms the reactors cooling agent. A cooling agent is usually water, but some nuclear reactors use liquid metal or molten salt. The cooling agent, heated by nuclear fission, produces steam. The steam turns turbines, or wheels turned by a flowing current. The turbines drive generators, or engines that create electricity.

Rods of material called nuclear poison can adjust how much electricity is produced. Nuclear poisons are materials, such as a type of the element xenon, that absorb some of the fission products created by nuclear fission. The more rods of nuclear poison that are present during the chain reaction, the slower and more controlled the reaction will be. Removing the rods will allow a stronger chain reaction and create more electricity.

About 15 percent of the worlds electricity is generated by nuclear power plants. The United States has more than 100 reactors, although it creates most of its electricity from fossil fuels and hydroelectric energy. Nations such as Lithuania, France, and Slovakia create almost all of their electricity from nuclear power plants.

Nuclear Food: Uranium

Uranium is the fuel most widely used to produce nuclear energy. That’s because uranium atoms split apart relatively easily. It’s also a very common element, found in rocks all over the world. However, the specific type of uranium used to produce nuclear energy, called U-235, is rare. U-235 makes up less than one percent of the uranium in the world.

Although some of the uranium the United States uses is mined in this country, most is imported. The U.S. gets uranium from Australia, Canada, Kazakhstan, Russia, and Uzbekistan. Once uranium is mined, it must be extracted from other minerals. It must also be processed before it can be used. 
Because nuclear fuel can be used to create nuclear weapons as well as nuclear reactors, only nations that are part of the Nuclear Non-Proliferation Treaty (NPT) are allowed to import uranium or plutonium, another nuclear fuel. The treaty promotes the peaceful use of nuclear fuel, as well as limiting the spread of nuclear weapons.

A typical nuclear reactor uses about 59,000 metric tons (65,000 tons) of uranium every year. Complex processes allow some uranium and plutonium to be re-enriched or recycled. This reduces the amount of mining, extracting, and processing that needs to be done.

Nuclear Energy and People

Nuclear energy produces electricity that can be used to power homes, schools, businesses, and hospitals. The first nuclear reactor to produce electricity was located near Arco, Idaho, in the U.S. The Experimental Breeder Reactor began powering itself in 1951. The first nuclear power plant designed to provide energy to a community was established in Obninsk, Russia, in 1954.

Building nuclear reactors requires a high level of technology, and only the countries that have signed the Nuclear Non-Proliferation Treaty can get the uranium or plutonium that is required. For these reasons, most nuclear power plants are located in the developed world. 

Nuclear power plants produce renewable, clean energy. They do not pollute the air or produce greenhouse gases. They can be built in urban or rural areas, and do not radically alter the environment around them.

The steam powering the turbines and generators is ultimately recycled. It is cooled down in a separate structure called a cooling tower. The steam turns back into water and can be used again to produce more electricity. Excess steam is simply recycled into the atmosphere, where it does no harm as clean water vapor.

However, the byproduct of nuclear energy is radioactive material. Radioactive material is a collection of unstable atomic nuclei. These nuclei lose their energy and can affect many materials around them, including organisms and the environment. Radioactive material can be extremely toxic, causing burns and increasing the risk for cancers, blood diseases, and bone decay.

Radioactive waste is what is left over from the operation of a nuclear reactor. Radioactive waste is mostly protective clothing worn by workers, tools, and cloths that have been in contact with radioactive dust. Radioactive waste is long-lasting. Materials like clothes and tools can stay radioactive for thousands of years. The government regulates how these materials are disposed of so they don’t contaminate anything else. 

Used fuel and rods of nuclear poison are extremely radioactive. The used uranium pellets must be stored in special containers that look like large swimming pools. Water cools the fuel and insulates the outside from contact with the radioactivity. Some nuclear plants store their used fuel in dry storage tanks above ground.

The storage sites for radioactive waste have become very controversial in the United States. For years, the government planned to construct an enormous nuclear waste facility near Yucca Mountain, Nevada, for instance. Environmental groups and local citizens protested the plan. They worried about radioactive waste leaking into the water supply and the Yucca Mountain environment, about 130 kilometers (80 miles) from the large urban area of Las Vegas, Nevada. Although the government began investigating the site in 1978, it stopped planning for a nuclear waste facility in Yucca Mountain in 2009. 

Chernobyl

Critics of nuclear energy worry that the storage facilities for radioactive waste will leak, crack, or erode. Radioactive material could then contaminate the soil and groundwater near the facility. This could lead to serious health problems for the people and organisms in the area. All communities would have to be evacuated.

This is what happened in Chernobyl, Ukraine, in 1986. A steam explosion at one of the power plants four nuclear reactors caused a fire, called a plume. This plume was highly radioactive, creating a cloud of radioactive particles that fell to the ground, called fallout. The fallout spread over the Chernobyl facility, as well as the surrounding area. The fallout drifted with the wind, and the particles entered the water cycle as rain. Radioactivity traced to Chernobyl fell as rain over Scotland and Ireland. Most of the radioactive fallout fell in Belarus.

The environmental impact of the Chernobyl disaster was immediate. For kilometers around the facility, the pine forest dried up and died. The red color of the dead pines earned this area the nickname the Red Forest. Fish from the nearby Pripyat River had so much radioactivity that people could no longer eat them. Cattle and horses in the area died.

More than 100,000 people were relocated after the disaster, but the number of human victims of Chernobyl is difficult to determine. The effects of radiation poisoning only appear after many years. Cancers and other diseases can be very difficult to trace to a single source.